Molecular Testing for Malaria Standard Operating Procedure (SOP)

Agarose Gel Electrophoresis of msp1, msp2 and glurp.

Document ID: EXT 07

WWARN Clinical Group

WorldWide Antimalarial Resistance Network (WWARN)

www.wwarn.org

Suggested citation: Clinical Group, WWARN. 2015.  Agarose Gel Electrophoresis of msp1, msp2 and glurp v1.1

Procedure ID: EXT 07

This procedure was developed by:

WWARN Clinical Group

WorldWide Antimalarial Resistance Network

University of Maryland School of Medicine

Mahidol University

Global Scientific Solutions

Version History

| Version number | Revision(s) & reason for amendment | Date of release |
| --- | --- | --- |
| 1.0 | Creation of procedure | 3 Jan 2012 |
| 1.1 | Added minor text; format different from other procedures | 10 Mar 2015 |

For more information, contact: 	
clinical@wwarn.org

WorldWide Antimalarial Resistance Network (WWARN)

www.wwarn.org

### Molecular Testing for Malaria: Overview of Standards

A number of consensus-adopted standards have been used in the development of this document. These include:

- MORU Standard Operating Procedure: Gel Electrophoresis (Watcharee, Naowarat, Supatchara, & Sarun, 2009).

- Recommended Genotyping Procedures (RGPs) to identify parasite populations (World Health Organization, 2007).

- MMV Guide to Malaria Genotyping (World Health Organization, 2008).

- Biosafety in Microbiological and Biomedical Laboratories (BMBL) 5th Edition (U.S. Department of Health and Human Services, 2007).

### Signature Page

By signing this page, staff members providing malaria recrudescence versus reinfection testing confirm they have read this SOP and guarantee to implement the procedures contained within.

| Name | Designation/affiliation | Signature | Date of signing |
| --- | --- | --- | --- |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |

### Version History

This SOP may be adapted to suit the particular needs of the individual laboratory. It is important to bear in mind that the purpose of an SOP is to ensure testing quality and result reproducibility.

| Version number | Revision(s) & reason for amendment | Date of approval | Approved by (lab supervisor / manager) |
| --- | --- | --- | --- |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |

### Contents

Molecular Testing for Malaria: Overview of Standards	3

Signature Page	4

Version History	5

Contents	6

1.	Scope	7

2.	Abbreviations	7

3.	Personnel qualifications	7

3.1.	Medical fitness	7

3.2.	Education and training	7

4.	Procedure	7

4.1.	Principle	8

4.2.	Samples	8

4.3.	Required Materials and Equipment	8

4.4.	Procedural steps	10

5.	Quality Control	11

6.	Procedure limitations	12

7.	Interpretation and Reporting of Results	12

8.	Safety Precautions	12

9.	Bibliography	17

10.	Appendices	19

Appendix A – Bench Top Reference	20

# Scope

This SOP describes the method used to separate and visualize amplified products from msp1, msp2 and glurp PCR.

# Abbreviations

bp	Base pairs

DBS	Dried Blood Spot

glurp	Glutamate rich protein gene

ml	millilitre

mM	milimolar

msp1	Merozoite surface protein gene 1

msp2	Merozoite surface protein gene 2

M	Molar

nPCR	Nested Polymerase chain reaction

PCR	Polymerase chain reaction

SOP	Standard Operating Procedure

(L	microlitre

# Personnel qualifications

## Medical fitness

Occupational health programs should be in place to monitor/address staff vaccinations and deal with exposures to potentially infected materials.

## Education and training

Training must be given on the following topics:

- Wearing and use of personal protective equipment and clothing;

- Handling of potentially infectious materials;

- Prevention of incidents and steps to be taken by workers in case incidents (including biological, chemical, electrical and fire hazards) occur;

- Procedures;

- Waste management;

- Impact of results for patient management and research.

Training must be provided:

- When a new staff member takes up post;

- Annually;

- When there is a change in conditions or best practices.

# Procedure

## Principle

Gel electrophoresis is the method of size-separating DNA fragments using an electric field. DNA is negatively charged and will migrate towards a positive charge when suspended in an appropriate matrix.

Agarose gel provides an appropriate matrix. An agarose gel is created by suspending dry agarose in a buffer solution, boiling until becomes clear, pouring it into a casting tray and allowing it to cool until set.

Several factors influence how fast the DNA migrates. These include:

- DNA molecule size

- Amperage used

- Concentration of agarose in the gel.

After electrophoresis the DNA is stained with a DNA binding agent (ethidium bromide) and visualized under UV light.

## Samples

Samples used in the SOP are derived from msp1 (SOP-05), msp2 (SOP-06) and glurp (SOP-07) PCR.

## Required Materials and Equipment

0.5 x TBE (1 L) (Add 900 ml distilled water to 100 ml 5 x TBE)

1 x Gel loading dye

Ethidium bromide (10 mg/ml stock solution)

Agarose powder

Gel tray (casting mold) with comb for 13 samples

Electrophoresis chamber and power pack

Microwave or boiling water bath

Clean piece of parafilm or similar strong disposable plastic or small tubes

1-20 (l single channel automatic pipette and tips

UV transilluminator

Fine tip marker pen

Table 1. Solutions commonly required for gel electrophoresis.

| Stock Solution | Ingredient | Quantity |
| --- | --- | --- |
| 5 x TBE (1 L) | Tris-HCL | 54 g |
|  | Boric acid | 27.5 g |
|  | 0.5 M EDTA pH 8.0 (186.12 g EDTA disodium salt in 1 L) | 20 ml |
|  | Distilled water | Make up to 1 L |
| 1 x Gel loading buffer (100 ml) | 30 ml glycerol |  |
|  | 10 mM Tris-HCl pH 7.5 | 0.16 g |
|  | 10 mM EDTA pH 8.0 | 0.37 g |
|  | Bromophenol blue | 0.25 g |
|  | Xylene cyanol | 0.25 g |
|  | Distilled water | Make up to 100 ml |
| Ethidium bromide (10 mg/ml) (store in 1-2 ml aliquots) | Dilute ethidium bromide liquid stock accordingly | Make up 10 ml |
| 1 kb ladder (if using pre-diluted ladder, follow manufacturer’s recommendation on quantity) | Gel loading buffer | 300 (l |
|  | 1 kb ladder stock (1 (g/(l) | 100 (l |
|  | Distilled water | 600 (l |

## Procedural steps

Important points to remember: Ethidium bromide is a known carcinogen. Take special care not to contaminate yourself and laboratory work surfaces. Take care when pipetting to prevent sample mix up. Always follow the worksheet order when loading gels.

Review sample worksheet and cross check samples. NB. It is very easy to make errors as gels cannot be labeled.

Gather all required supplies and samples.

Preparation of agarose gels NB. Products from msp2 and glurp PCR are run on 2% agarose gels. Products from msp1 PCR are run on 3% agarose gels. Dissolve agarose in 0.5 x TBE by heating the mixture in a microwave or boiling waterbath until all the agarose particles have dissolved. PCR Quantity of agarose required / gel volume 50 ml 100 ml 150 ml msp2 & glurp 1 g 2 g 3 g msp1 1.5 g 3 g 4.5 g NB. Add the agarose powder to 0.5 x TBE with constant swirling to prevent clumping of agarose.

Cool to approximately 50 ºC. Assemble gel tray with comb/s and pour in molten agarose. Leave at room temperature for 30 min to set. Remove well-forming comb/s. Pour 0.5 x TBE over gel to cover it completely.

Loading the gel. Label appropriate number of tubes or positions along parafilm according to sample worksheet order. Pipette 1 (l of gel loading buffer into each tube or onto the parafilm. Mix 4 (l each sample with the gel loading buffer and load into a separate well on the gel. NB. Paired samples (Day 0 and post treatment) must be run side by side on the gel. Load the P2 and N2 controls NB. The N0 control must be loaded onto at least one gel. Load 5 (l of the DNA ladder. NB. The ladder must be run either side of the gel. If the gel is very wide, load additional ladder every 10 samples. Run the gel according to manufacturer’s recommendations for the particular power pack and gel apparatus. The gel is ready for staining when the dye front reaches to within 1 cm of the gel end.

Staining the gel. Immerse the gel in ethidium bromide staining solution (10 (l ethidium bromide stock solution in 100 ml 0.5 x TBE) for 30 min. NB. Staining solution may be used for approximately 2 weeks if kept in the dark at room temperature.

View the gel using the UV transilluminator and take a photograph using a digital camera. NB. UV safety goggles must be worn when working at the UV transilluminator.

# Quality Control

Reagents should be prepared and stored according to this SOP. Storage conditions should be checked twice daily and temperatures recorded on a daily temperature chart.

  - Negative Control

- The N0 (DNA extraction control) need only be run on a gel once to confirm the absence of contamination.

- The N1 (pPCR) controls do not need to be run and should be saved in case of any problems. N1 controls can be used to verify the absence of contamination in the pPCR in case of any problems with nPCR.

- The N2 (nPCR) controls must always be run with nPCR samples. These confirm the absence of contamination throughout the entire process.

  - Positive Control

- The P1 (pPCR) controls do not need to be run and should be saved in case of any problems. P1 controls can be used to verify the success of pPCR in case of any problems with nPCR.

- The P2 (nPCR) controls must always be run with nPCR samples. These confirm the success of the entire process.

# Procedure limitations

- The quality of the DBS sample is of critical importance for every step of recrudescence versus reinfection testing.

- Poor quality samples and/or insufficient DNA extraction may result in a lack of PCR products and/or spurious bands.

- The appropriate quality-assured storage of reagents and samples is also critical to ensure the highest quality PCR results.

- Standard procedures should be followed exactly at all times. This will ensure the highest quality reproducible results are obtained.

# Interpretation and Reporting of Results

Result interpretation is described in SOP-09 Manual Scoring of Recrudescence Versus Reinfection Results.

# Safety Precautions

Toxic chemicals, irritants, carcinogens and non-ionizing radiation are used in this SOP (see table 2). Precautions must be taken to ensure personnel and work area safety.

Table 2. Hazardous materials used in gel electrophoresis.

| Material | Hazards | Precautions | First Aid |
| --- | --- | --- | --- |
| Ethidium Bromide | May be fatal if inhaled. Harmful if swallowed of absorbed through skin. Causes irritation to skin, eyes and respiratory tract. May cause heritable genetic damage. | Goggles Lab coat Fume hood Gloves | Inhalation: If inhaled, remove to fresh air. If not breathing, give artificial respiration. If breathing is difficult, give oxygen. CALL A PHYSICIAN IMMEDIATELY. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Get medical attention. Skin Contact: Immediately flush skin with plenty of water for at least 15 minutes. Remove contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention if irritation develops. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting upper and lower eyelids occasionally. Get medical attention if irritation persists. |
| Agarose | Nuisance dust | Goggles Lab coat | Inhalation: Remove to fresh air. Get medical attention for any breathing difficulty. Ingestion: Give several glasses of water to drink to dilute. If large amounts were swallowed, get medical advice. Skin Contact: Wash exposed area with soap and water. Get medical advice if irritation develops. Eye Contact: Wash thoroughly with running water. Get medical advice if irritation develops. |
| Tris-HCl | Harmful if swallowed, may cause irritation to eyes and skin | Goggles Lab coat Gloves Ventilated Fume hood | Inhalation: Remove to fresh air. Get medical attention for any breathing difficulty. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Get medical attention. Skin Contact: Immediately flush skin with plenty of water for at least 15 minutes. Remove contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention if irritation develops. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting upper and lower eyelids occasionally. Get medical attention if irritation persists. |
| Boric Acid | Harmful if swallowed or inhaled, causes irritation to eyes, skin and respiratory tract. Affects central nervous system, liver and kidneys. | Goggles Lab coat Gloves Fume hood | Inhalation: Remove to fresh air. If not breathing, give artificial respiration. If breathing is difficult, give oxygen. Call a physician. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Skin Contact: Remove any contaminated clothing. Wash skin with soap or mild detergent and water for at least 15 minutes. Get medical attention if irritation develops or persists. Wash clothing before re-use. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting lower and upper eyelids occasionally. Get medical attention immediately. |
| EDTA | Harmful if swallowed or inhaled, causes irritation to eyes, skin and respiratory tract. | Goggles Lab coat Gloves | Inhalation: Remove to fresh air. Get medical attention for any breathing difficulty. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Get medical attention. Skin Contact: Immediately flush skin with plenty of water for at least 15 minutes. Remove contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention if irritation develops. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting upper and lower eyelids occasionally. Get medical attention if irritation persists. |
| Bromo-phenol blue | Harmful if swallowed or inhaled, causes irritation to eyes, skin and respiratory tract. | Goggles Lab coat Gloves | Inhalation: Remove to fresh air. Get medical attention for any breathing difficulty. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Get medical attention. Skin Contact: Immediately flush skin with plenty of water for at least 15 minutes. Remove contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention if irritation develops. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting upper and lower eyelids occasionally. Get medical attention if irritation persists. |
| Xylene cyanol | May cause eye, skin, and respiratory tract irritation. May be harmful if swallowed, inhaled, or absorbed through the skin. The toxicological properties of this material have not been fully investigated | Goggles Lab coat Gloves | Inhalation: Remove to fresh air. Get medical attention for any breathing difficulty. Ingestion: Induce vomiting immediately as directed by medical personnel. Never give anything by mouth to an unconscious person. Get medical attention. Skin Contact: Immediately flush skin with plenty of soap and water for at least 15 minutes. Remove contaminated clothing and shoes. Wash clothing before reuse. Thoroughly clean shoes before reuse. Get medical attention if irritation develops. Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes, lifting upper and lower eyelids occasionally. Get medical attention if irritation persists. |

Always practice universal precautions (treat all patient specimens as potentially infectious material:

- Wear good quality, single-use, disposable medical examination gloves.

- Wear a laboratory coat or gown.

- Wash hands after removal of gloves.

Universal precautions always apply in the laboratory environment. In addition, laboratory staff should:

- Wear sturdy, closed-toe shoes;

- Put on protective eye wear for high-risk activities such as working with UV light;

- Refrain from drinking, eating, smoking and storing food anywhere in the laboratory; and

- Remove gloves and wash hands before touching clean areas such as door handles, lift/elevator buttons and telephones.

# Bibliography

Calderaro, A., Piccolo, G., Perandin, F., Gorrini, C., Peruzzi, S., Zuelli, C., et al. (2007). Genetic polymorphisms influence Plasmodium ovale PCR detection accuracy. Journal of Clinical Microbiology, 45(5), 1624-1627.

Cattamanchi, A. A., Kyabayinze, D., Hubbard, A., & Rosenthal, P. J. (2003). Distinguishing recrudescence from reinfection in a longitudinal antimalarial druf efficacy study: comparison of results based on genotyping of msp-1, msp-2, and glurp. American Journal of Tropical Medicine, 68(2), 133-139.

Centers for Disease Control and Prevention. (2006). Blood collection - finger prick. Retrieved August 17, 2010, from CDC HIV Training: http://wwwn.cdc.gov/dls/ila/hivtraining/trainersguide/pdf/presentations/Module8Presentation.pdf

Clinical and Laboratory Standards Institute. (2007). Blood collection on filter paper for newborn screening programs; approved standard - fifth edition. CLSI document LA4-A5, 27(20).

Falk, N., Maire, N., Sama, W., Owusu-Agyei, S., Smith, T., & Beck, H.-P. a. (2006). Comparison of PCR-RFLP and Genescan-based genotyping for analyzing infection dynamics of Plasmodium falciparum. American Journal of Tropical Medicine., 74(6), 944-950.

Färnert, A., Arez, A. P., Babiker, H. A., Beck, H. P., Benito, A., Björkman, A., et al. (n.d.).

Färnert, A., Arez, A. P., Babiker, H. A., Beck, H. P., Benito, A., Björkman, A., et al. (n.d.). Genotyping of Plasmodium falciparum infections by PCR: a comparative multicentre study. Trans R Soc Trop Med Hyg., 95.

Kyes, S., Craig, A. G., & Marsh, K. a. (1993). Plasmodium falciparum: a method for the amplification of S antigens and its application to laboratory and field samples. Experimental Parasitology, 71, 473-483.

Nakeesathit, S., Pagomrat, W., Tanomsing, N., & Hanchana, S. a. (2001). DNA Extraction. Bangkok: Mahidol Oxford Tropical Medicine Research Unit.

Plowe, C. V., Djimde, A., Bouare, M., & Doumbo, O. a. (1995). Pyrimethamine and proguanil resistance-conferring mutations in Plasmodium falciparum dihydrofolate reductase: polymerase chain reaction methods for surveillance in Africa. American Journal of Tropical Medicine and Hygiene., 52, 565-568.

Program for Appropriate Technology in Health (PATH). (2005). RBP-EIA: collecting, processing, and handling venous, capillary, and blood spot samples. Seattle: PATH.

QIAGEN. (2007). QIAamp DNA mini and blood mini handbook Second edition. QIAGEN.

Rubio, J. M., J., R. P., L., B. M., Garcia, M., M., M., & I., E. M. (1999). Semi-nested. multiplex polymerase chain reaction for detection of human malaria parasites and evidence of Plasmodium vivax infection in Equatorial Guinea. American Journal of Tropical Medicine and Hygiene., 60, 183-187.

U.S. Department of Health and Human Services. (2007). Biosafety in microbiological and biomedical laboratories. 5th. Washington, District of Columbia, USA: U. S. Government Printing Office.

U.S. Department of Health and Human Services. (2007). Biosafety in microbiological and biomedical laboratories (5th ed.). Washington, District of Columbia, USA: U. S. Government Printing Office.

Watcharee, P., Naowarat, T., Supatchara, N., & Sarun, H. a. (2009). Gel Electrophoresis. Bangkok: MORU.

World Health Organization. (2007). Methods and techniques for clinical trials on antimalarial drug efficacy: genotyping to identify parasite populations. Amsterdam: WHO.

World Health Organization. (2007). Recommended Genotyping Procedures (RGPs) to identify parasite populations. Amsterdam: Medicines for Malaria Venture and World Health Organization.

World Health Organization. (2008). Consultation on Technical and Operational Recommendations for Clinical Laboratory Testing Harmonization and Standardization. Geneva: World Health Organization.

Worldwide Antimalarial Resistance Network. (2010). Filter paper preparation v1.0 (SOP ID: MOL03/CLIN06). Worldwide Antimalarial Resistance Network (WWARN).

Zwetyenga, J., Rogier, C., Tall, A., Fontenille, D., Snounou, G., & Trape, J.-F. a.-P. (1998). No influence of age on infectious complexity and allelic distribution in Plasmodium falciparum infections in Ndiop, a Senegalese village with seasonal, mesoendemic malaria. American Journal of Tropical Medicine and Hygiene., 59(5), 726-735.

# Appendices

### Appendix A – Bench Top Reference

Molecular Testing for Malaria (MTM) Bench Top Reference

Gel Electrophoresis - Document ID: BTR-08

Review sample worksheet and cross check samples. Gather all required supplies and samples.

Preparation of agarose gels NB. Products from msp2 and glurp PCR are run on 2% agarose gels. Products from msp1 PCR are run on 3% agarose gels. Dissolve agarose in 0.5 x TBE by heating the mixture in a microwave or boiling waterbath until all the agarose particles have dissolved. PCR Quantity of agarose required / gel volume 50 ml 100 ml 150 ml msp2 & glurp 1 g 2 g 3 g msp1 1.5 g 3 g 4.5 g

Cool to approximately 50 ºC. Assemble gel tray with comb/s and pour in molten agarose. Leave at room temperature for 30 min to set. Remove well-forming comb/s. Pour 0.5 x TBE over gel to cover it completely.

Loading the gel. Label appropriate number of tubes or positions along parafilm according to sample worksheet order. Pipette 1 (l of gel loading buffer into each tube or onto the parafilm. Mix 4 (l each sample with the gel loading buffer and load into a separate well on the gel. NB. Paired samples (Day 0 and post treatment) must be run side by side on the gel. Load the P2 and N2 controls NB. The N0 control must be loaded onto at least one gel. Load (l of the DNA ladder. NB. The ladder must be run either side of the gel. If the gel is very wide, load an additional ladder for every 10 samples. Run the gel according to manufacturer’s recommendations for the particular power pack and gel apparatus. The gel is ready for staining when the dye front reaches to within 1cm of the gel end.

Staining the gel. Immerse the gel in ethidium bromide staining solution (10 (l ethidium bromide stock solution in 100 ml 0.5 x TBE) for 30 min.

View the gel using the UV transilluminator and take a photograph using a digital camera. NB. UV safety goggles must be worn when working at the UV transilluminator.

# Footnotes

Stable for 1 year at +4 ºC in a dark container.

Ethidium bromide is extremely toxic by inhalation therefore, do not use the powdered form in the laboratory. Ethidium bromide solutions are available and should be purchased.

Always seek medical attention if large doses are inhaled, digested or if any irritation appears on contact.

# Text boxes

In association with the Mekong Molecular Surveillance for Drug Resistant Malaria program, supported by USAID

In association with the Mekong Molecular Surveillance for Drug Resistant Malaria program, supported by USAID