Molecular Testing for Malaria Standard Operating Procedure (SOP)

Manual size estimation of msp1, msp2 and glurp

PCR products on gel

Document ID: SOP-09

Developed by:

# Molecular Testing for Malaria: Overview of Standards

A number of consensus-adopted standards have been used in the development of this document. These include:

- Recommended Genotyping Procedures (RGPs) to identify parasite populations (World Health Organization, 2007).

- MMV Guide to Malaria Genotyping (World Health Organization, 2008).

- Biosafety in Microbiological and Biomedical Laboratories (BMBL) 5th Edition (U.S. Department of Health and Human Services, 2007).

# Signature Page

By signing this page, staff members providing malaria recrudescence versus reinfection testing confirm they have read this SOP and guarantee to implement the procedures contained within.

| Name | Designation/affiliation | Signature | Date of signing |
| --- | --- | --- | --- |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |
|  |  |  | [DD/MM/YYY] |

# Version History

This SOP may be adapted to suit the particular needs of the individual laboratory. It is important to bear in mind that the purpose of an SOP is to ensure testing quality and result reproducibility.

| Version number | Revision(s) & reason for amendment | Date of approval | Approved by (lab supervisor / manager) |
| --- | --- | --- | --- |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |
|  |  | [DD/MM/YYY] |  |

Contents

Molecular Testing for Malaria: Overview of Standards	2

Signature Page	3

Version History	4

1.	Scope	6

2.	Abbreviations	6

3.	Personnel qualifications	6

3.1.	Medical fitness	6

3.2.	Education and training	6

4.	Procedure	7

4.1.	Principle	7

4.2.	Samples	7

4.3.	Required Materials and Equipment	7

4.4.	Procedural steps	8

5.	Quality Control	14

6.	Procedure limitations	15

7.	Interpretation and Reporting of Results	15

8.	Safety Precautions	16

9.	Bibliography	17

Appendices	20

Appendix A – Figure 3 Enlarged.	21

Appendix B – Bench Top Reference	22

Appendix C – Recrudescence versus Reinfection Worksheet	24

# Scope

This SOP describes the method of manually determining the sizes of recrudescence versus reinfection PCR products.

# Abbreviations

bp	Base pairs

DBS	Dried Blood Spot

glurp	Glutamate rich protein gene

ml	millilitre

msp1	Merozoite surface protein gene 1

msp2	Merozoite surface protein gene 2

nPCR	Nested Polymerase chain reaction

PCR	Polymerase chain reaction

SOP	Standard Operating Procedure

(L	microlitre

# Personnel qualifications

## Medical fitness

Occupational health programs should be in place to monitor/address staff vaccinations and deal with exposures to potentially infected materials.

## Education and training

Training must be given on the following topics:

- Wearing and use of personal protective equipment and clothing;

- Handling of potentially infectious materials;

- Prevention of incidents and steps to be taken by workers in case incidents (including biological, chemical, electrical and fire hazards) occur;

- Procedures;

- Waste management;

- Impact of results for patient management and research.

Training must be provided:

- When a new staff member takes up post;

- Annually;

- When there is a change in conditions.

# Procedure

## Principle

This SOP describes how to score and interpret Plasmodium falciparum genotyping results from msp1, msp2 and glurp PCR products to distinguish between new and recrudescent infections.

This procedure is used in place of band-scoring gel electrophoresis software and follows on from:

SOP-08 Agarose Gel Electrophoresis of PCR Products

## Samples

The samples are the products of primary and secondary PCR from msp1 (SOP-05), msp2 (SOP-06) and glurp (SOP-07) amplification. The products are subjected to electrophoresis according to SOP-08 and the resulting gel is used to determine the final test result.

## Required Materials and Equipment

UV Trans-illuminator

Safety goggles/eye goggles (must be UV-protective)

Disposable gloves

Pen, pencil, ruler

Camera or digital camera with hood

## Procedural steps

Important points to remember: Bands must be bright and sharp to be of high enough quality for scoring. PCRs must be repeated if bands appear in the negative control. Products under 100 bp should be excluded from result interpretation. Size determination must always be performed by two readers and their results compared.

After gel electrophoresis (see SOP-08), place the gel on a UV trans-illuminator and take a photo. NB. If a digital camera is used, print the photo, preferably on photo-quality paper.

Lay the photo on a clean, level surface.

Using a ball-point pen or pencil, mark each gel with the date, tester’s initials and the PCR marker used e.g. msp1, msp2, glurp.

Using a ball-point pen or pencil, mark each lane with the sample identifier (from the PCR worksheet in SOP-05, 06 and/or 07).

Mark the DNA ladder on at least one side of the gel.

A properly labeled gel should look like this:

Confirmation of controls. Check each gel to confirm the sizes of the positive controls (see figure 2 a-f and table 1 below for examples). NB. Review important points overleaf. Record each result on the corresponding worksheet. NB. Remember to record all results on the same batch worksheet used throughout sample accessioning and PCR.

Figure 2. Confirming correct sizes of positive controls. A: msp1 K1 PCR on Pf strains 3D7, K1, RO33, 7G8 and Dd2 B: msp1 MAD20 PCR on Pf strains D10, Dd2, W2, D6 and 3D7 C: msp1 RO33 PCR on Pf strains RO33, Dd2, 7G8, D6 and 3D7 D: msp2 FC27 PCR on Pf strains 3D7, K1, RO33, D10 and Dd2 E: msp2 3D7/IC PCR on Pf strains 3D7, K1, RO33, D10 and 024 F: glurp PCR on Pf strains 3D7, K1, RO33, D10 and 024

Important points: The product sizes in figure 2 were obtained using MORU primer pairs for each PCR reaction (see Appendix E in SOP-05, SOP-06 and SOP-07). If using different primers, it is necessary to perform PCR on the positive control DNA used in the laboratory and determine the size for each product. The results should be recorded in the table below and saved in this SOP for reference purposes.

Table 1. Expected product sizes for positive controls using MORU primers. Template DNA Locus / Strain msp1 msp2 glurp K1 MAD20 RO33 FC27 3D7/IC N/A 3D7 250 500 900 7G8 160 D6 250 D10 180 320 550 800 Dd2 220 400 K1 180 380 850 RO33 160 480 1000 W2 220

Table 2. Expected product sizes for positive controls using (insert name of lab) primers (( marks where template DNA is suitable for PCR). Template DNA Locus / Strain msp1 msp2 glurp K1 MAD20 RO33 FC27 3D7/IC N/A 3D7 ( ( ( 7G8 ( ( ( D6 ( ( ( D10 ( ( ( Dd2 ( ( ( FC27 ( ( ( HB3 ( ( ( K1 ( ( ( MAD20 ( ( RO33 ( ( ( W2

Check each gel to confirm the absence of product in the negative control lanes. NB. PCR products in the negative control lanes indicate a problem with the PCR protocol. The results must be recorded as “INVALID” and corrective actions must be taken. Always make a record of invalid results and the steps taken to correct any problems. Record each result on the corresponding worksheet. NB. Remember to record all results on the same batch worksheet used throughout sample accessioning and PCR.

Determination of PCR product size in samples. An appropriately labeled, high quality gel is critical for the accurate size determination of PCR products.

Important points: Day 0 and post-treatment samples must be run side by side on the gel. Each PCR product should be well-defined and easy to visualize. Markers should show sharp, defined bands. Samples, controls and markers should run uniformly in the horizontal plane (i.e. no smiling or frowning gels). To be a ‘new infection,’ all alleles in the post-treatment sample must be different from those in the Day 0 sample. To be ‘recrudescence,’ at least one allele at each locus is the same in the Day 0 and post-treatment samples.

Once the control data is recorded and verified as acceptable, record the product sizes for each sample pair on the corresponding worksheet. NB. Remember to maintain the same worksheet for each batch of samples throughout the DNA extraction, PCR and scoring processes.

Examples of PCR product size determination in samples. The following section provides an example of determining recrudescence versus reinfection from 5 pairs of samples taken from patients A, B, C and D. Each pair is labeled according to when it was collected. Day 0 (D0) indicating the baseline sample or Day X (Dx) indicating the post-treatment sample.

Figure 3. Example gels showing PCR products from samples A-D NB. A larger version of this figure is shown in Appendix A. A: msp1 K1 PCR on samples A-D using 3D7 DNA for positive control B: msp1 MAD20 PCR on samples A- D using Dd2 DNA for positive control C: msp1 RO33 PCR on samples A- D using RO33 DNA for positive control D: msp2 FC27 PCR on samples A- D using K1 DNA for positive control E: msp2 3D7/IC PCR on samples A- D using 3D7 DNA for positive control F: glurp PCR on samples A- D using 3D7 DNA for positive control

Use the MMV algorithm (World Health Organization, 2007) to determine recrudescence from reinfection: Figure 4. The MMV algorithm for determining recrudescence versus reinfection.

Record product sizes and results on the worksheet and store for future reference. Table 3. Recrudescence versus reinfection test results of samples from figure 3. Date Staff Initials 1-Jul-2010 MI No. Sample ID PCR Product Sizes (bp) for control, indicate band sizes or leave blank Results / Comment msp1 msp2 glurp K1 MAD20 RO33 FC27 3D7/IC 1 A0 200 400 750 Recrudescence 2 Ax 200 400 750 3 B0 170,220 500 950 New infection 4 Bx 200 190 550,600 1000 5 C0 180 160 800 Recrudescence 6 Cx 180 160 800 7 D0 180 350 800 New infection 8 Dx 250 180 300 800 9 10 11 N0 No bands - OK 12 N1 n/a 13 P1 n/a 14 N2 No bands - OK 15 P2 250 220 160 380 500 900 Correct sizes

# Quality Control

  - Negative Control

- The N0 (DNA extraction control) need only be run on a gel once to confirm the absence of contamination.

- The N1 (pPCR) controls do not need to be run and should be saved in case of any problems. N1 controls can be used to verify the absence of contamination in the pPCR in case of any problems with nPCR.

- The N2 (nPCR) controls must always be run with nPCR samples. These confirm the absence of contamination throughout the entire process.

  - Positive Control

- The P1 (pPCR) controls do not need to be run and should be saved in case of any problems. P1 controls can be used to verify the success of pPCR in case of any problems with nPCR.

- The P2 (nPCR) controls must always be run with nPCR samples. These confirm the success of the entire process.

# Procedure limitations

- The quality of the DBS sample is of critical importance for every step of recrudescence versus reinfection testing.

- Poor quality samples and/or insufficient DNA extraction may result in a lack of PCR products and/or spurious bands.

- The appropriate quality-assured storage of reagents and samples is also critical to ensure the highest quality PCR results.

- PCR procedures should be followed exactly at all times. This will ensure the highest quality reproducible results are obtained.

# Interpretation and Reporting of Results

Results are reported on the worksheet in Appendix C. The worksheet is used throughout the testing process including sample receipt, DNA extraction, PCR, gel electrophoresis and interpretation of results.

# Safety Precautions

Although extracted DNA is a low biohazard risk specimen, always practice universal precautions (treat all patient specimens as potentially infectious material:

- Wear good quality, single-use, disposable medical examination gloves.

- Wear a laboratory coat or gown.

- Wash hands after removal of gloves.

Universal precautions always apply in the laboratory environment. In addition, laboratory staff should:

- Wear sturdy, closed-toe shoes;

- Put on protective eye wear for high-risk activities such as working with UV light;

- Refrain from drinking, eating, smoking and storing food anywhere in the laboratory; and

- Remove gloves and wash hands before touching clean areas such as door handles, lift/elevator buttons and telephones.

# Bibliography

Calderaro, A., Piccolo, G., Perandin, F., Gorrini, C., Peruzzi, S., Zuelli, C., et al. (2007). Genetic polymorphisms influence Plasmodium ovale PCR detection accuracy. Journal of Clinical Microbiology, 45(5), 1624-1627.

Cattamanchi, A. A., Kyabayinze, D., Hubbard, A., & Rosenthal, P. J. (2003). Distinguishing recrudescence from reinfection in a longitudinal antimalarial druf efficacy study: comparison of results based on genotyping of msp-1, msp-2, and glurp. American Journal of Tropical Medicine, 68(2), 133-139.

Centers for Disease Control and Prevention. (2006). Blood collection - finger prick. Retrieved August 17, 2010, from CDC HIV Training: http://wwwn.cdc.gov/dls/ila/hivtraining/trainersguide/pdf/presentations/Module8Presentation.pdf

Clinical and Laboratory Standards Institute. (2007). Blood collection on filter paper for newborn screening programs; approved standard - fifth edition. CLSI document LA4-A5, 27(20).

Falk, N., Maire, N., Sama, W., Owusu-Agyei, S., Smith, T., & Beck, H.-P. a. (2006). Comparison of PCR-RFLP and Genescan-based genotyping for analyzing infection dynamics of Plasmodium falciparum. American Journal of Tropical Medicine., 74(6), 944-950.

Färnert, A., Arez, A. P., Babiker, H. A., Beck, H. P., Benito, A., Björkman, A., et al. (n.d.).

Färnert, A., Arez, A. P., Babiker, H. A., Beck, H. P., Benito, A., Björkman, A., et al. (n.d.). Genotyping of Plasmodium falciparum infections by PCR: a comparative multicentre study. Trans R Soc Trop Med Hyg., 95.

Kyes, S., Craig, A. G., & Marsh, K. a. (1993). Plasmodium falciparum: a method for the amplification of S antigens and its application to laboratory and field samples. Experimental Parasitology, 71, 473-483.

Nakeesathit, S., Pagomrat, W., Tanomsing, N., & Hanchana, S. a. (2001). DNA Extraction. Bangkok: Mahidol Oxford Tropical Medicine Research Unit.

Plowe, C. V., Djimde, A., Bouare, M., & Doumbo, O. a. (1995). Pyrimethamine and proguanil resistance-conferring mutations in Plasmodium falciparum dihydrofolate reductase: polymerase chain reaction methods for surveillance in Africa. American Journal of Tropical Medicine and Hygiene., 52, 565-568.

Program for Appropriate Technology in Health (PATH). (2005). RBP-EIA: collecting, processing, and handling venous, capillary, and blood spot samples. Seattle: PATH.

QIAGEN. (2007). QIAamp DNA mini and blood mini handbook Second edition. QIAGEN.

Rubio, J. M., J., R. P., L., B. M., Garcia, M., M., M., & I., E. M. (1999). Semi-nested. multiplex polymerase chain reaction for detection of human malaria parasites and evidence of Plasmodium vivax infection in Equatorial Guinea. American Journal of Tropical Medicine and Hygiene., 60, 183-187.

U.S. Department of Health and Human Services. (2007). Biosafety in microbiological and biomedical laboratories. 5th. Washington, District of Columbia, USA: U. S. Government Printing Office.

U.S. Department of Health and Human Services. (2007). Biosafety in microbiological and biomedical laboratories (5th ed.). Washington, District of Columbia, USA: U. S. Government Printing Office.

Watcharee, P., Naowarat, T., Supatchara, N., & Sarun, H. a. (2009). Gel Electrophoresis. Bangkok: MORU.

World Health Organization. (2007). Methods and techniques for clinical trials on antimalarial drug efficacy: genotyping to identify parasite populations. Amsterdam: WHO.

World Health Organization. (2007). Recommended Genotyping Procedures (RGPs) to identify parasite populations. Amsterdam: Medicines for Malaria Venture and World Health Organization.

World Health Organization. (2008). Consultation on Technical and Operational Recommendations for Clinical Laboratory Testing Harmonization and Standardization. Geneva: World Health Organization.

Worldwide Antimalarial Resistance Network. (2010). Filter paper preparation v1.0 (SOP ID: MOL03/CLIN06). Worldwide Antimalarial Resistance Network (WWARN).

Zwetyenga, J., Rogier, C., Tall, A., Fontenille, D., Snounou, G., & Trape, J.-F. a.-P. (1998). No influence of age on infectious complexity and allelic distribution in Plasmodium falciparum infections in Ndiop, a Senegalese village with seasonal, mesoendemic malaria. American Journal of Tropical Medicine and Hygiene., 59(5), 726-735.

# Appendices

## Appendix A – Figure 3 Enlarged.

## Appendix B – Bench Top Reference

Molecular Testing for Malaria (MTM) Bench Top Reference

Manual Scoring of Results - Document ID: BTR-09

After gel electrophoresis (see SOP-08), place the gel on a UV trans-illuminator and take a photo. NB. If a digital camera is used, print the photo, preferably on photo-quality paper.

Lay the photo on a clean, level surface.

Using a ball-point pen or pencil, mark each gel with the date, testers initials and the PCR marker used e.g. msp1, msp2, glurp.

Using a ball-point pen or pencil, mark each lane with the sample identifier (from the PCR worksheet in SOP-05, 06 and/or 07).

Mark the DNA ladder on at least one side of the gel.

Check each gel to confirm the sizes of the positive controls and record on the worksheet.

Check each gel to confirm the absence of product in the negative control lanes and record on the worksheet.

Once the control data is recorded and verified as acceptable, record the product sizes for each sample pair on the corresponding worksheet.

Use the MMV algorithm (World Health Organization, 2007) to determine recrudescence from reinfection:

Record product sizes and results on the worksheet and store for future reference.

## Appendix C – Recrudescence versus Reinfection Worksheet

| Date | Initials |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Number | Sample ID | PCR Product Sizes (bp) for control, indicate band sizes or leave blank | Comments & Results |
|  |  | msp1 | msp2 | glurp |  |
|  |  | K1 | MAD20 | RO33 | FC27 | 3D7/IC |  |  |
| 1 |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |  |  |
| 11 | N0 |  |  |  |  |  |  |  |
| 12 | N1 |  |  |  |  |  |  |  |
| 13 | P1 |  |  |  |  |  |  |  |
| 14 | N2 |  |  |  |  |  |  |  |
| 15 | P2 |  |  |  |  |  |  |  |

# Text boxes

In association with the Mekong Molecular Surveillance for Drug Resistant Malaria program, supported by USAID

Figure 4. Labeling the gel.

Date and staff initials

PCR (locus and strain)

Lanes clearly marked

DNA marker /ladder

indicated

100

200

300

400

500

600

700

800

900

1000

1500

Msp1 K1  1-Jul-2010 PJF

M  A0 Ax B0 Bx C0 Cx D0 Dx  P2 N0 N2  M

F

E

D

A

C

B